## Slide 1: NSM
Incident Response

## Slide 2: Network Traffic
Before we get to NSM we need to talk about network traffic
  What it looks like
  How it behaves
  ”Normal”
Wireshark is one of our primary tools that we’ll use
Network Security Monitoring
  Data we need for finding malicious events

## Slide 3: Wireshark
Packet & protocol analyzer
Great tool for inspecting network traffic
  Doesn’t scale particularly well, but best for learning
  You may have used it before, but if you haven’t that’s fine
Rare: Works well cross platform
Packet Sniffer
  Works ok, not great
Uses the libpcap library
  Allows us to filter

## Slide 4: Where to use it
Troubleshooting
  Troubleshooting
    Troubleshooting
Why something behaves the way it does
Is traffic moving the way we think it is?
  Whether this is to check if we’re getting traffic at all or if parts of the packet are getting formed the way we think they’re getting formed
    Ping example
Learning!

## Slide 5: Wireshark Capturing
Not great for long term capturing
It captures all data as a frame
  Hopefully it knows how to correctly decode the data
  It knows about a bunch of different protocols
  Sometimes it doesn’t
Do we want to capture in promiscuous mode?
  Does this let us see everything?
  Do we want to see everything?
Wifi?

## Slide 6: Where things are captured

## Slide 7: Capture Buffer

## Slide 8: Bigger Network Interfaces
Notes: A lot of NICs can handle a lot of traffic
Dropping frames can confuse traffic
  Handling buffers is very important

## Slide 9: Speeding up Wireshark
Increase the buffer size
Don’t do dynamic screen updates
Don’t resolve names
Get a better computer
Stop other things that are running

## Slide 10: Capture Filters
Allow you to limit what is being captured
  Does this help or hurt our ability to capture more data without dropping packets?
host 10.1.1.1
host 192.168.0.1 and host 10.1.1.1
tcp port http
ip
not broadcast not multicast
ether host 00:04:13:00:09:a3

## Slide 11: Capture vs Display Filter
Capture filter just limits what’s captured
  Helpful, but not that helpful
Display filters
  Completely different format

## Slide 12: Cautions of Wireshark
Reading bug logs, you’ll see security fixes
Isn’t the best “enterprise” capture tool
  Again, good for troubleshooting
Don’t run as administrator
  Especially opening outside files

## Slide 13: Theory of NSM
Typically
  Log blocked network traffic
  Allow other things to flow freely
Backwards
  Why?
Where does NSM not work?
Large volumes of data
Encrypted data
Privacy???

## Slide 14: Types of Data to look at in NSM
Full content
  Everything
Extracted content
  Files
Session
  Who is talking to who
Transaction
  Who is saying what
Statistics
  Common occurrence vs this never happens
Metadata
  Data about data
Alerts

## Slide 15: Challenges with NSM
So why do we even need it?
It can be expensive
Very time consuming
It doesn’t actually prevent anything
We have IPS for that
Prevention isn’t that great
  Firewall prevents, IDS detect

## Slide 16: 4 Rules to Realize
All of our current “systems have flaws that make them vulnerable
We can’t replace the “systems” we’re using right now
We can’t make a perfect ”system”
Even the perfect “system” can be compromised by an insider, willingly or not
  No, it doesn’t always have to be on purpose

## Slide 17: NSM’s Value
Post—occurrence value
If we’re 100% secure, NSM is useless
  Everyone thinks they are 100% secure, nobody is
NSM: Detect bad things
NSM: Reproduce attackers traces
NSM: What did they do?
  What did they steal?
  How bad is it?
  This informs the rest of the steps as you’re responding

## Slide 18: Summary
NSM is essential, but often overlooked
  Because it doesn’t ”prevent”
Typical security measures are ineffective
  Defensive security only goes so far
  Remember back to planning when I said we do defensive security to reduce attacks?
    We don’t eliminate them
We need the ability to reconstruct events
  Network forensics/heuristics

## Slide 19: Wireshark demo And a lab too