## Slide 1: Number Systems
Lesson 10

## Slide 2: Learning Outcomes
Upon completion of this lesson, students will be able to:
  Differentiate between different number systems used by computing systems
  Demonstrate the ability to convert between different number systems – base 2, 10 and 16
  Examine how negative values are stored and interpreted in computing systems

## Slide 3: Why Should You Care?
Values in computing are almost never displayed in decimal format
Most values that are seen in IDA are in the hexadecimal format
Machines can only interpret binary data
Being able to recognize what base/format a value is in can be valuable

## Slide 4: How Does a Processor Work?
From addition, you can implement multiplication and division and shifts
Now have a variety of ops acting on 1 or more inputs
  Division, mult, addition, subtraction, logical AND, logical OR, logical XOR, Shift left, shift right
Now we want to use them:
  Bring in inputs and perform operations on them
  CPU has registers, more about these later
Encode operations in a bit pattern
  0001 = perform NOT
  0010 = perform AND
  0100 = perform Addition

## Slide 5: How Does a Processor Work?
We want to add 6 and 2
  Send it instruction for add: 0100
  Send it 6 and 2 in binary: 0110 and 0010
  So: 0100 0110 0010
Now we have a sequence of operations
This is machine language and is hard!
So we develop assembly languages
  Assembly compiles to machine language
  Have mnemonics that map to machine code
  ADD EAX, 2
  ADD 6 2

## Slide 6: Decimal
Standard base-10 number system
10 single digit numerical values ranging from 0 to 9
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9

## Slide 7: Binary
Base-2 number system
2 single digit numerical values: 0 and 1
A single digit of binary is a bit, 8 of these bits is a byte
0 | 1
Notes: Example being a light switch of 1 being on and 0 being off

## Slide 8: Hexadecimal
Base-16 number system
10 numerical values and 6 alphabetic values
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F

## Slide 9: Converting Decimal to Binary
1000 Base-10 to Base-2
Start from the right side to the left
Binary:
Division | Remainder
1000/2=500 | 0
 |  |  |  |  |  |  |  |  | 0

## Slide 10: Converting Decimal to Binary
1000 Base-10 to Base-2
Start from the right side to the left
Binary:
Division | Remainder
1000/2=500 | 0
500/2=250 | 0
 |  |  |  |  |  |  |  | 0 | 0

## Slide 11: Converting Decimal to Binary
1000 Base-10 to Base-2
Start from the right side to the left
Binary:
Division | Remainder
1000/2=500 | 0
500/2=250 | 0
250/2=125 | 0
 |  |  |  |  |  |  | 0 | 0 | 0

## Slide 12: Converting Decimal to Binary
1000 Base-10 to Base-2
Start from the right side to the left
Binary:
Division | Remainder
1000/2=500 | 0
500/2=250 | 0
250/2=125 | 0
125/2=62 | 1
 |  |  |  |  |  | 1 | 0 | 0 | 0

## Slide 13: Converting Decimal to Binary
1000 Base-10 to Base-2
Start from the right side to the left
Binary:
Division | Remainder
1000/2=500 | 0
500/2=250 | 0
250/2=125 | 0
125/2=62 | 1
62/2=31 | 0
 |  |  |  |  | 0 | 1 | 0 | 0 | 0

## Slide 14: Converting Decimal to Binary
1000 Base-10 to Base-2
Start from the right side to the left
Binary:
Division | Remainder
1000/2=500 | 0
500/2=250 | 0
250/2=125 | 0
125/2=62 | 1
62/2=31 | 0
31/2=15 | 1
 |  |  |  | 1 | 0 | 1 | 0 | 0 | 0

## Slide 15: Converting Decimal to Binary
1000 Base-10 to Base-2
Start from the right side to the left
Binary:
Division | Remainder
1000/2=500 | 0
500/2=250 | 0
250/2=125 | 0
125/2=62 | 1
62/2=31 | 0
31/2=15 | 1
15/2=7 | 1
 |  |  | 1 | 1 | 0 | 1 | 0 | 0 | 0

## Slide 16: Converting Decimal to Binary
1000 Base-10 to Base-2
Start from the right side to the left
Binary:
Division | Remainder
1000/2=500 | 0
500/2=250 | 0
250/2=125 | 0
125/2=62 | 1
62/2=31 | 0
31/2=15 | 1
15/2=7 | 1
7/2=3 | 1
 |  | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0

## Slide 17: Converting Decimal to Binary
1000 Base-10 to Base-2
Start from the right side to the left
Binary:
Division | Remainder
1000/2=500 | 0
500/2=250 | 0
250/2=125 | 0
125/2=62 | 1
62/2=31 | 0
31/2=15 | 1
15/2=7 | 1
7/2=3 | 1
3/2=1 | 1
 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0

## Slide 18: Converting Decimal to Binary
1000 Base-10 to Base-2
Start from the right side to the left
Binary:
Division | Remainder
1000/2=500 | 0
500/2=250 | 0
250/2=125 | 0
125/2=62 | 1
62/2=31 | 0
31/2=15 | 1
15/2=7 | 1
7/2=3 | 1
3/2=1 | 1
1/2=0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0

## Slide 19: Converting Binary to Decimal
Each binary digit has an equivalent decimal value: 2n (n being the slot)
If the value in that digit is 1 then that decimal value is part of the whole decimal number
Convert 1111101000 to decimal
512 + 256 + 128 + 64 + 32 + 8=1000
1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1

## Slide 20: Converting Decimal to Hex
1000 Base-10 to Base-16
Since 14 is larger than 9 it enters the alphabetic characters(E)
1000 base-10 in hex is 3E8
Division | Remainder
1000/16=62 | 8
62/16=3 | 14
3/16=0 | 3
1
2
3

## Slide 21: Converting Hex to Decimal
3E8 Base-16 to Base-10
768+224+8=1000
Index | Calculation | Output
2 | 3x162 | 768
1 | 14x161 | 224
0 | 8x160 | 8

## Slide 22: Converting Hex to Binary
Convert 0xFACE Base-16 to Base-2
First, convert the Alphabetic values into the equivalent decimal value
Then convert each of the decimal values to binary
F | A | C | E
15 | 10 | 12 | 14
Hex | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
Decimal | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
15 | 10 | 12 | 14
1111 | 1010 | 1100 | 1110

## Slide 23: Integer Representations
There are several ways to represent negative integers
  Sign Magnitude
  One’s Compliment
  Two’s Compliment

## Slide 24: Sign Magnitude
The first bit of the number represents the sign, then the rest is the actual value
A first bit as 1 is negative, the first bit as 0 is positive
Take: 0001 0101 using sign magnitude
The decimal value is 21
Take: 1001 0101 using sign magnitude
The decimal value would be -21

## Slide 25: One’s Compliment
Again, for the first bit, 0 is positive, 1 is negative
To get the decimal value if positive nothing changes
To get the decimal value if it’s negative, flip all the bits (negate)
Original | First Bit | Bits After Flip (if first bit is 1) | Decimal Value | After Negation (if first bit is 1)
0011 | 0 | 0011 | 3 | 3
1100 | 1 | 0011 | 3 | -3
1010 | 1 | 0101 | 5 | -5

## Slide 26: Two’s Compliment
Again, for the first bit, 0 is positive, 1 is negative
To get the decimal value if positive nothing changes
To get the decimal value if negative, flip all the bits and add 1
Original | First Bit | Bits After Flip (if first bit is 1) | Decimal Value | Add 1 (if first bit is 1) | After Negation (if first bit is 1)
0011 | 0 | 0011 | 3 | 3 | 3
1100 | 1 | 0011 | 3 | 0100 | -4
1010 | 1 | 0101 | 5 | 0110 | -6
Notes: This is used in most cases

## Slide 27: Summary
Upon completion of this lesson, students will be able to:
  Differentiate between different number systems used by computing systems
  Demonstrate the ability to convert between different number systems – base 2, 10 and 16
  Examine how negative values are stored and interpreted