## Slide 1: Session 3: SoftWARE Tools
Tommy Morris
Professor, Electrical and Computer Engineering
Director, Center for Cybersecurity Research and Education
University of Alabama in Huntsville

## Slide 2: Tools to InSTALL
OpenPLC Runtime
OpenPLC Editor
Arduino IDE
  OpenPLC Arduino Firmware
SCADABr Image
Virtual Box

## Slide 3: OpenPLC + ArDUINO+PC
OpenPLC runtime runs on PC.
Arduino provides Input/Output (IO): Analog and Digital
Inputs: buttons, sensors (various)
Outputs: LED, relays, speakers, etc.
Host only network from Virtual Box or lab network.

## Slide 4: OpenPLC Runtime
This is the PLC application.
The runtime is platform specific. OpenPLC runs on many platforms.
  Linux, Windows, Raspberry PI, and others.
  Select your platform at https://www.openplcproject.com/runtime
  Select one to download
When using OpenPLC with Arduino your PC hosts the runtime. In other words, your PC is the PLC in this case. The Arduino is a slave device for I/O connectivity.
Use the OpenPLC runtime for your operating system. Linux and Windows are supported. 32-bit and 64-bit versions are supported.
The downloaded file is an executable. Download and run to install.
Flash drive: OpenPLC Installer x64.exe

## Slide 5: OPENPLC Runtime and Editor in the Start Menu

## Slide 6: Arduino IDE
The IDE is the Arduino programming and debugging environment.
OpenPLC runs firmware on the Arduino to access its GPIO (General Purpose Input Output) and A/D (Analog to Digital) pins.
Download the IDE here:
  https://www.arduino.cc/en/Main/Software
  Be sure to choose the IDE, not the web editor.
Flash drive: arduino-1.8.9-windows.exe

## Slide 7: Arduino OpenPLC Firmware
The Arduino OpenPLC Firmware must be installed and executed on the Arduino.
The Arduino Firmware is available here:
  https://www.openplcproject.com/getting-started-arduino
Choose the firmware for UNO.
The download is a ZIP file.
  Extract the Zip
Open the firmware in the Arduino IDE and open in the Arduino IDE (select the OpenPLC_Uno.ino when opening).
Upload the firmware to the Arduino
  Connect your USB cable
CTRL-U to upload (or press the → button)
Flash drive: OpenPLC_Uno_v3.zip
Tools -> Port
Set COM3

## Slide 8: OPENPLC Editor
The OpenPLC Editor is available at:
  https://www.openplcproject.com/plcopen-editor
  Choose the version for your host PC.
Instructions for Windows
  Download, unzip, and double-click on the OpenPLC Editor shortcut.
  Note: The windows version of the editor comes with the runtime installer. No need to download and install this separate for Windows.
Instructions for Linux
  Download, unzip, and run on terminal: ./install.sh
  Once the installation finishes, a shortcut for OpenPLC Editor will be created on the Applications menu.

## Slide 9: SCADABR
SCADABr is distributed as a Virtual Box VM image.
Links are available for Virtual Box and the SCADABr .ova file at https://www.openplcproject.com/reference-installing-scadabr
Virtual Box: https://www.virtualbox.org/wiki/Downloads
SCADABr ova: https://drive.google.com/file/d/1gEOZmN9_Nt5shXy4iYS1z_EMxB4r0Kzh/view?usp=sharing

## Slide 10: SCADABR
Virtual Box Installation
  Download the .exe for your host.
  Run the .exe file and follow directions from the installer.
SCADABr .ova installation
  Run Virtual Box from the start menu
  Use File -> Import Appliance
  Select your .ova file
  Change the network setting to

## Slide 11: Virtual Box Network Setting
While the SCADABr VM is off
  select Settings
  then select Network
  Set “Attached to:” to “Host-only Adapter”
The Host Only IP address can be found (and set) under Preferences -> Network -> Host Only Networks
  Select the appropriate adapter
  You will need this IP to connect SCADABr from your host’s browser the PLC running on your host.

## Slide 12: Starting up
Build your circuit and connect to the Arduino Uno pins
Build your Ladder Logic and save it
Launch the Arduino IDE
  Upload the OpenPLC firmware
Launch the OpenPLC runtime
  Run the application from the start menu
  In your host’s browser open localhost:8080 - this is the OpenPLC configuration port
Launch the SCADABr HMI
  Start the SCADABr VM.
  Read the SCADABr URL from the VM (should be http://192.168.56.101:8080/ScadaBR)
  Open the URL in your host’s browser
Repeat every time you run.

## Slide 13: RunTIME ERROR
Some participants got an error similar to “Verifying Installation. Press any key to exit.”
Fix: Reinstall Cygwin manually and rebase
  Download https://cygwin.com/setup-x86_64.exe
  Install: install directory: c:\users\%USERNAME%\openplc\runtime
  Select all defaults
Run start menu -> OpenPLC -> Rebase OpenPLC (this take a while)
Try the runtime again

## Slide 14: Passwords
OpenPLC website: http://localhost:8080
  User:openplc
  Pass: openplc
SCADA Br website: https://192.168.56.101:8080/ScadaBr (or similar IP)
  User: admin
  Pass: admin
Virtual SCADA VM
  User:scada
  Pass: scada

## Slide 15: OPENPLC DASHBOARD
Access the OpenPLC dashboard via your host’s browser.
  URL: http://localhost:8080/
  User: openplc, Password: openplc (change in Users menu)
Common functions from the dashboard
  Start/Stop the PLC
  Load/Remove programs
  Add Slave Device

## Slide 16: Load a Program
Select “Programs” on the left hand side menu
Choose a file (suffix .st)
Select “Upload Program”
  On the next screen
    give the program a name and description (optional)
    press “Upload program”
  After the compile finishes, select “Go to dashboard”
  Select “Start PLC” on the left hand side

## Slide 17: Remove a Program
Select “Programs” on the left hand side menu
Select an existing program from the table
Select “Remove program”
Note: “Reload program” will recompile the program. Do not use this with a new version.
When you have a new version
  Remove the old version (to avoid confusion)
  Upload the new version

## Slide 18: Add a Slave Device
From the OpenPLC Dashboard select “Slave Devices” on the left hand side menu
Select “Add New Device”
On the next screen
  Name your device
  Set device type to Arduino Uno
  Select the appropriate COM port (should be COM3)
  Click “Save Device”

## Slide 19: Placing Components in OpenPLC Editor
Left click the component icon
Left click the location in the ladder section for the component

## Slide 20: ExerCISE 1
Complete the exercise from https://www.openplcproject.com/reference-your-first-project
Note: there is no HMI for this exercise.