## Slide 1: Breadboarding Circuits for OpenPLC
Dr. David J. Coe
Electrical and Computer Engineering Department
University of Alabama in Huntsville
coed@uah.edu

## Slide 2: Outline
Introduction to Arduino
Arduino-OpenPLC Setup
Breadboarding of Circuits
References

## Slide 3: Introduction to Arduino

## Slide 4: What is an Arduino?
An open source electronics platform for building cyber-physical systems
  Cyber-physical systems sense and interact with their surroundings
https://store.arduino.cc/usa/arduino-uno-rev3
Arduino Uno
~$22

## Slide 5: Arduino Uno R3 Pinout
https://www.circuito.io/blog/arduino-uno-pinout/

## Slide 6: Arduino Uno R3 – OpenPLC Pinout
https://www.openplcproject.com/getting-started-arduino
Slave devices start at 100 so add 100
Example: %IX100.0

## Slide 7: Arduino-OpenPLC Setup

## Slide 8: Download OpenPLC Firmware for Arduino Uno
Download firmware from
https://www.openplcproject.com/getting-started-arduino

## Slide 9: Breadboarding of Circuits

## Slide 10: Circuit Schematic
+V
OpenPLC Slave
Arduino Uno R3
PB1
PB2
R2
%IX100.0
%QX100.0
R3
LED1
%IX100.1
R1
+V is 5Volts for the Arduino
PB1 and PB2 are momentary pushbuttons
R1 = R2 = R3 = 1 k Ohm resistor
LED1 is a light emitting diode (LED)
Ground

## Slide 11: Circuit Components – Prototyping Breadboards
http://wiring.org.co/learning/tutorials/breadboard/

## Slide 12: Cyber-Physical Systems: Circuit Hints
Breadboard your circuit before powering up the Arduino or Raspberry Pi
  Check it carefully before applying power
  Double check against the pinout diagrams
Be mindful of component voltage levels
  Some may be 5V, others 3.3V
  Routing 5V into a 3.3V device is usually bad
  Level translation may be required
Learn to interpret the component datasheets
  Look at min/max voltages and currents
  May provide sample circuits that illustrate use of a particular component
Invest in a multimeter for measuring voltages, currents, resistance, and continuity

## Slide 13: Cyber-Physical Systems: Circuit Hints
Most processor General Purpose Input/Output (GPIO) pins are not designed to drive low impedance/low resistance loads
  Relay, solenoid, and motor coils require a driver circuit that can supply more current than the GPIO pins
  LEDs typically require a series resistor to limit current draw
    Resistor too large allows too little current flow (dim LED)
    Resistor too small or non-existent allows too much current flow (bad)
  Failure to limit current sourcing/sinking through GPIO pins may result in permanent damage to the Raspberry Pi (or Arduino)
Relay/solenoid coils may require a parallel diode to dissipate back EMF (current flowing from collapsing magnetic field)

## Slide 14: Circuit Components – Resistors - 1
+ V -
I
+ V -
I
Ohm’s Law
Voltage = Current x Resistance
V = I x R
I = V / R = 3.3 volts/1000 ohm = 3.3 milliamps (mA)
I = V / R = 5.0 volts/1000 ohm = 5.0 milliamps (mA)
Current calculations for 1k ohm resistor with 5 V and 3.3 V circuits

## Slide 15: Circuit Components – Resistors - 2
https://learn.sparkfun.com/tutorials/resistors
Sample output from online resistance calculator at URL below
Photograph of 1 kOhm resistor
https://sites.google.com/site/kmitl58010166/home/lab-i-basic-resistive-circuit-calculations-and-measurements

## Slide 16: Circuit Components - Diodes
https://cdn.sparkfun.com/assets/learn_tutorials/7/5/backwardsDiode.png
Light Emitting Diode (LED)
Signal Diode
https://www.electronics-tutorials.ws/diode/diode_4.html
“one-way current check valve”

## Slide 17: Circuit Components - Pushbuttons
https://components101.com/switches/push-button
Switch Open
(Normally Open)
Switch Closed
(Switch Pressed)
A
B
A
B
A
B
A
B

## Slide 18: References
The OpenPLC Project
  https://www.openplcproject.com/
Horowitz and Hill, The Art of Electronics 2nd ed.
  Good overview of digital and analog circuits with many examples including interfacing to sensors and actuators such as those in a cyber-physical system