## Slide 1: Lesson 01 Programmable Logic Controllers and Ladder Logic Programming
Dr. David J. Coe
Electrical and Computer Engineering Department
University of Alabama in Huntsville
coed@uah.edu

## Slide 2: Outline
Introduction to PLCs
Ladder Logic Programming
OpenPLC Editor
Suggested Reading
Hands-On Laboratory Exercise #1

## Slide 3: Introduction to PLCs

## Slide 4: Programmable Logic Controllers (PLCs)
Programmable Logic Controller (PLC)
  An embedded computing platform that uses sensors to perceive the state of the physical system and actuators to modify that state according to a control algorithm

## Slide 5: Overview PLC Operation - 1
Input Table
Output Table
Physical Inputs
Physical Outputs
Control Algorithm
Step 1
At the beginning of the cycle, the PLC perceives the state of the physical system by reading the physical inputs and storing those values in the input table
Comments
Physical inputs may change before current cycle is complete
Cycle time is chosen such that the amount of input change will be negligible before beginning of next cycle
PLC

## Slide 6: Overview PLC Operation - 2
Input Table
Output Table
Physical Inputs
Physical Outputs
Control Algorithm
Step 2
The control algorithm uses values from input table to compute the outputs which are stored in the output table
PLC

## Slide 7: Overview PLC Operation - 3
Input Table
Output Table
Physical Inputs
Physical Outputs
Control Algorithm
Step 3
At the end of the cycle, the values from the output table are written to the physical outputs to exercise control over the system
Comments
At the beginning of the next cycle, the PLC will repeat this three-step sequence again starting with Step 1
PLC

## Slide 8: Cycle Time
Cycle time duration is driven by the physics of the physical system (and the computing capabilities of the PLC)
  A system whose state changes very slowly over time can have a longer cycle time
    Example: Electric water heater
          Slow to empty, slow to reheat
  A system whose state changes rapidly will require a much shorter cycle time so the PLC can maintain control of the physical system
    Example: First stage of a liquid-fueled rocket
          Rapid change in speed, altitude, and mass

## Slide 9: Control Algorithm Representation
The OpenPLC platform is compatible with all five standard representations of control algorithm logic (as defined by IEC-61131-3) including
  Ladder Logic (LD)
  Structured Text (ST)
  Instruction List (IL)
  Function Block Diagram (FBD)
  Sequential Function Chart (SFC)
The OpenPLC Editor converts all representations into Structured Text prior to compilation
Today we will focus on Ladder Logic
https://www.openplcproject.com/reference-what-is-a-plc

## Slide 10: Ladder Logic Programming

## Slide 11: What is Ladder Logic?
Ladder Logic
  A graphical programming language derived from relay (ladder) logic
  A relay is a switch operated by an actuator such as an electromagnet

## Slide 12: Ladder Logic Structure
Ladder logic consists of a sequence of one or more ladder rungs
  Each rung includes one or more contacts or function blocks and one or more coils along with rails
    Rails are sources or sinks of electric current
      Left rail is at a positive voltage (current source)
      Right rail at ground (current sink)
    Contacts may be inputs or computed intermediate values
    Coils are outputs
  A given rung is interpreted left-to-right as drawn
  The rungs are processed in the order they appear in the ladder logic diagram top-to-bottom

## Slide 13: Sample Ladder Logic Rung
( )
Push Button
Lamp
Contact
Coil
Left Rail (+)
Right Rail (-)

## Slide 14: Ladder Logic Symbols - 1
Normally Open Contact (NO)
Mechanical spring holds A-B switch open
Energized electromagnet coil overpowers spring to close switch
Logic 1 (positive voltage) energizes electromagnet coil
Logic 0 (zero voltage) allows spring to dominate
https://ladderlogicworld.com/relay-logic-vs-ladder-logic/
A
A
B
B
No path for current to flow from A to B
Current may now flow from A to B
Ladder Logic Symbol

## Slide 15: Ladder Logic Symbols - 2
https://ladderlogicworld.com/relay-logic-vs-ladder-logic/
A
A
B
B
No path for current to flow from A to B
Current may now flow from A to B
Normally Closed Contact (NC)
Mechanical spring holds A-B switch closed
Energized electromagnet coil overpowers spring to open switch
Logic 1 (positive voltage) energizes electromagnet coil
Logic 0 (zero voltage) allows spring to dominate
Ladder Logic Symbol

## Slide 16: Ladder Logic Symbols - 3
Coil
An output or external load such as an actuator (motor, heater, etc.) or annunciator (bulb, LED, etc.)
Logic 1 (positive voltage) energizes coil
Logic 0 (zero voltage) de-energizes coil
( )
Ladder Logic Symbol

## Slide 17: Ladder Logic Symbols - 4
Negated Coil
A output or external load such as an actuator (motor, heater, etc.) or annunciator (bulb, LED, etc.)
Logic 1 (positive voltage) de-energizes coil
Logic 0 (zero voltage) energizes coil
( )
Ladder Logic Symbol

## Slide 18: Ladder Logic Symbols - 5
Function Blocks
Many different function blocks available
  Timers
  Adders
  Multiplexers
  Memory
  Etc.

## Slide 19: Sample Ladder Logic in OpenPLC Editor
Sample use of constant block and timer block

## Slide 20: OpenPLC Editor

## Slide 21: Install OpenPLC Editor
https://www.openplcproject.com/plcopen-editor

## Slide 22: Enter Ladder Logic - 1
1. Create new project
2. Create new project folder

## Slide 23: Enter Ladder Logic - 2
Select LD for a Ladder Logic program

## Slide 24: Enter Ladder Logic - 3
1. Set Project and Product names
2. Set Company name

## Slide 25: Enter Ladder Logic - 4
Verify default Task (task0) and Instance (instance0) created

## Slide 26: Enter Ladder Logic - 5
Select program0 to see ladder logic editor
Ladder Logic Toolbar

## Slide 27: Enter Ladder Logic - 6
Hit green plus sign to add program variables
(Note: These are Raspberry Pi location values)

## Slide 28: Enter Ladder Logic - 7
All variables created – locations correspond to physical hardware pins
%IX is an input
%QX is an output

## Slide 29: Enter Ladder Logic - 8
1. Create left rail with two pins
2. Create right rail with one pin

## Slide 30: Enter Ladder Logic - 9
1. Create Push Button #1
2. Create Push Button #2

## Slide 31: Enter Ladder Logic - 10
1. Create 2 second constant (2000 msec)
2. Drag and drop on-delay timer (TON) function block

## Slide 32: Enter Ladder Logic - 11
1. Add LED output coil
2. Click and drag to define wire connections

## Slide 33: Suggested Reading
The OpenPLC Project
  https://www.openplcproject.com/
Tommy Morris – Six SCADA Modules
  https://clark.center/details/tommy_morris/Six%20SCADA%20Modules

## Slide 34: Hands-On Laboratory Exercise #1

## Slide 35: Laboratory Exercise #1 Instructions - 1
Objective
  Learn how to use OpenPLC Editor to create a program using Ladder Logic

## Slide 36: Laboratory Exercise #1 Instructions - 2
Install OpenPLC Editor
Use OpenPLC Editor to enter the Ladder Logic for the First Project as described at the URL
https://www.openplcproject.com/reference-your-first-project
Adjust the Input/Output pin locations to match those on the OpenPLC slave Arduino Uno
Be sure to save your work
https://www.openplcproject.com/reference-your-first-project

## Slide 37: Laboratory Exercise #1 Instructions - 3
https://www.openplcproject.com/reference-your-first-project
Adjust these to match Arduino Uno OpenPLC slave

## Slide 38: Laboratory Exercise #1 Instructions - 4
Sample Deliverables
  Zip file of entire project folder
  Screenshots of Ladder Logic program