## Slide 1: Lesson 03 Code Generation and Deployment to OpenPLC
Dr. David J. Coe
Electrical and Computer Engineering Department
University of Alabama in Huntsville
coed@uah.edu

## Slide 2: Outline
Code Generation
Code Deployment
Suggested Reading
Hands-On Laboratory Exercise #3

## Slide 3: Code Generation

## Slide 4: Generate Structured Text - 1
Locate code generation menu button on toolbar

## Slide 5: Generate Structured Text - 2
Click on code generation menu button

## Slide 6: Generate Structured Text - 3
Select location to save code and enter filename

## Slide 7: Generate Structured Text - 4
Ladder Logic translated successfully into Structured Text

## Slide 8: Ladder Logic versus Structured Text

## Slide 9: Code Deployment

## Slide 10: Code Deployment to OpenPLC - 1
Use browser to access OpenPLC server on physical hardware
A different program is currently loaded and ready to execute

## Slide 11: Code Deployment to OpenPLC - 2
Go to Programs tab to select Choose File

## Slide 12: Code Deployment to OpenPLC - 3
Navigate file system and select new program to upload
Hit Upload Program to initiate file transfer to physical OpenPLC

## Slide 13: Code Deployment to OpenPLC - 4
Enter project name and description
Scroll down and hit Upload Program to initiate program compilation

## Slide 14: Code Deployment to OpenPLC - 5
Structured text version of program now compiled into C code
C code compiled into a binary executable

## Slide 15: Code Deployment to OpenPLC - 6
Compiled binary program now loaded into physical OpenPLC
Hit Start PLC to execute program

## Slide 16: Code Deployment to OpenPLC - 7
Compiled binary program now executing on physical OpenPLC
Hit Stop PLC to terminate program execution

## Slide 17: Code Deployment to OpenPLC - 8
Modbus is a legacy serial point-to-point PLC communication protocol
Modbus TCP wraps legacy Modbus packet in TCP wrapper
Port 502 is default port for Modbus TCP communications

## Slide 18: Suggested Reading
The OpenPLC Project
  https://www.openplcproject.com/
Tommy Morris – Six SCADA Modules
  https://clark.center/details/tommy_morris/Six%20SCADA%20Modules

## Slide 19: Hands-On Laboratory Exercise #3

## Slide 20: Laboratory Exercise #3 Instructions - 1
Objectives
  Learn how to use OpenPLC Editor to generate structured text implementation of the First Project Ladder Logic program
  Learn how to deploy the generated structured text program to the OpenPLC runtime
  Learn how to execute the compiled structured text program on the OpenPLC runtime

## Slide 21: Laboratory Exercise #3 Instructions - 2
Use OpenPLC Editor to simulate the First Project Ladder Logic as described at the URL
https://www.openplcproject.com/reference-your-first-project
Use the OpenPLC Editor code generation button to generate the structured text program from your ladder logic program
Configure your OpenPLC runtime instance
Use the browser to access your OpenPLC runtime instance and upload the structured text program
https://www.openplcproject.com/reference-your-first-project

## Slide 22: Laboratory Exercise #3 Instructions - 3
Sample Deliverables
  Zip file of entire project directory including structured text code
  Screenshots of ladder logic and structured text programs
  Screenshots of OpenPLC runtime showing successful compilation of structured text program
  Screenshots of OpenPLC runtime showing execution of fully compiled program