## Slide 1: Raspberry Pi and OpenPLC
Dr. David J. Coe
Electrical and Computer Engineering Department
University of Alabama in Huntsville
coed@uah.edu

## Slide 2: Outline
Introduction to Raspberry Pi
Raspberry Pi Preparation
OpenPLC Installation on Raspberry Pi
Sample OpenPLC - Raspberry Pi Project
Hints for Instructors
References
Hands-On Laboratory Exercise #5

## Slide 3: Introduction to Raspberry Pi

## Slide 4: What is a Raspberry Pi?
Family of low cost, single-board computers targeted at education
  Linux-based operating system called Raspbian OS
  Many models that differ by processing capabilities, memory, wired and wireless interfaces provided
  Often sold as part of a kit which may include a case, power supply, and other accessories such as a camera or prototyping breadboard
https://www.raspberrypi.org
$35 Raspberry Pi 3 B+
$10 Raspberry Pi Zero

## Slide 5: What can you do with a Raspberry Pi?
Learn computer programming
  Example: Python, C, C++, and more!
Learn about robotics and autonomous vehicles
  Example: Donkey Car open source self-driving vehicle
  https://www.donkeycar.com/
Learn image processing
  Example: OpenCV – Open Computer Vision
  https://www.learnopencv.com/install-opencv-4-on-raspberry-pi/
Learn about machine learning
  Example: Google’s Tensorflow machine learning tools
  https://www.tensorflow.org/install/source_rpi
Learn about cybersecurity
  Example: Kali Linux and its suite of cybersecurity tools
  https://www.offensive-security.com/kali-linux-arm-images/
Learn about Programmable Logic Controllers (PLCs) and Cybersecurity
  Example: OpenPLC Project by Thiago Alves
  https://www.openplcproject.com/

## Slide 6: Raspberry Pi 3 B+ Preparation

## Slide 7: Before Connecting Power to the Raspberry Pi 3 B+
Warning:
  If you are using the bare Raspberry Pi board without a case, be sure the board is NOT on a conductive surface when you connect the power supply or else…
    You may shock yourself if you are touching the conductive surface when you connect power to the Pi
    You may destroy your Raspberry Pi board by short circuiting wire traces on the board
  I recommend purchase of a plastic case for your Raspberry Pi board to protect both you and the Pi

## Slide 8: Before You Disconnect Power to the Raspberry Pi
Warning:
  Be sure to properly shutdown your Raspberry Pi prior to unplugging the power cord
  If not, you may corrupt the microSD card which will force you to rebuild the entire file system starting with installation of a clean copy of the Raspbian OS image onto the microSD card itself and a reinstall of OpenPLC
  I recommend using the Shutdown menu option on the Raspberry Pi desktop interface and waiting a few minutes before unplugging the power supply cord
    Hints:
    Backup any OpenPLC programs you wish to keep before shutdown – just in case
      Use the Linux (secure copy) utility scp
    On my setup, I wait until the monitor no longer thinks its connected to a computer and the last lights on the Pi stop blinking before I unplug the Pi power supply

## Slide 9: Before You Disconnect Power to the Raspberry Pi

## Slide 10: Preparation: Acquire a Raspberry Pi 3 B+ Kit
My Raspberry Pi 3 B+ kit included a microSD card with a preloaded Raspbian OS image
  Many sources for Raspberry Pi kits
    Sparkfun Electronics ( https://www.sparkfun.com )
    Adafruit ( https://www.adafruit.com )
    CanaKit ( https://www.canakit.com )
  Be sure the kit includes a case and a power supply at minimum
    To use the Raspberry Pi as a PLC, it will need to interface with physical world sensors and actuators
    Select a case that provides access to the 40-pin connector
    Hint:
    In addition to the Pi board, case, and power supply, get a kit that includes a prototyping board, ribbon cable, a breakout board for the 40-pin connector, and a selection of circuit components (resistors, capacitors, jumper wires, pushbutton switches, etc.)

## Slide 11: Photo: My Raspberry Pi 3 B+ Kit
https://www.canakit.com/raspberry-pi-3-model-b-plus-ultimate-kit.html

## Slide 12: Photo: Raspberry Pi 3 Breakout Board
Back
Front

## Slide 13: OpenPLC Pinout
https://www.openplcproject.com/getting-started-rpi
https://www.raspberrypi.org/documentation/usage/gpio/

## Slide 14: Photo: Breakout Board on Prototyping Breadboard
https://www.openplcproject.com/getting-started-rpi
https://www.jameco.com/Jameco/workshop/circuitnotes/raspberry-pi-circuit-note.html

## Slide 15: Connect Raspberry Pi 3 to Breakout Board
Ribbon cable to Raspberry Pi
Ribbon cable to breakout board
Ribbon cable keyed for plug in to breakout board
Align red wire of ribbon cable to pin #1 on Raspberry Pi 3B+ header

## Slide 16: Preparation: Boot Your Raspberry Pi 3 B+
Add a keyboard, monitor, and mouse
  You will need a keyboard, monitor, and mouse to configure WiFi network
Install the microSD card in the card slot
If the Raspberry Pi is not in a case, be sure it is not on a conductive surface
  Plug in power supply to wall power
  Hook power supply to Raspberry Pi
  Wait for Raspberry Pi to boot – you should see the Raspbian OS graphical desktop

## Slide 17: Booted Raspberry Pi 3 B+

## Slide 18: Preparation: Boot the Raspberry Pi 3 B+
The default credentials for logging into the Raspberry Pi are
  Username: pi
  Password: raspberry
These credentials are so common they already appear in Kali wordlists of common credentials for brute-force attacks
   Change your password!!!

## Slide 19: Open Terminal Window to Change Password
Use standard Linux passwd command to change password

## Slide 20: Configure WiFi - 1
Right-click WiFi Icon to reach network preferences

## Slide 21: Configure WiFi - 2
Select an interface and enter network parameters

## Slide 22: Update Raspbian OS
To update the Raspberry Pi software, use the following commands in your terminal window to apply any outstanding Raspbian OS patches and upgrades
  sudo apt-get update
  sudo apt-get upgrade

## Slide 23: Determine IP Address of Raspberry Pi
Use terminal window to determine the IP address of your Raspberry Pi
  Be sure to retain this information for later
  ifconfig

## Slide 24: OpenPLC Installation on Raspberry Pi 3 B+

## Slide 25: Installing OpenPLC Runtime on Pi
Browse to OpenPLC Project and follow provided instructions to install OpenPLC
  https://www.openplcproject.com/getting-started-rpi
Install Git
  sudo apt-get install git
Clone OpenPLC repository (I download the ZIP file directly from GitHub)
  git clone https://github.com/thiagoralves/OpenPLC_v3.git
Change directory into repository clone
  cd OpenPLC_v3
Run install script
  ./install.sh rpi
Test OpenPLC installation by browsing to the following URL
Pi_IP_Address_Goes_Here:8080

## Slide 26: Sample OpenPLC – Raspberry Pi Project

## Slide 27: Circuit Schematic
+V
OpenPLC Raspberry Pi
PB1
PB2
R2
%IX0.2
%QX0.0
R3
LED1
%IX0.3
R1
+V is 3.3Volts for the Raspberry Pi
PB1 and PB2 are momentary pushbuttons
R1 = R2 = R3 = 1 k Ohm resistor
LED1 is a light emitting diode (LED)
Ground

## Slide 28: Ladder Logic and Generated Structured Text

## Slide 29: Layout of Physical Circuit on Breadboard

## Slide 30: Ladder Logic and Generated Structured Text
https://www.openplcproject.com/getting-started-rpi
%IX0.2
%IX0.3
%QX0.0

## Slide 31: Circuit Components – Prototyping Breadboards
http://wiring.org.co/learning/tutorials/breadboard/

## Slide 32: Cyber-Physical Systems: Circuit Hints
Breadboard your circuit before powering up the Raspberry Pi
  Check it carefully before applying power
  Double check against the pinout diagrams
Be mindful of component voltage levels
  Some may be 5V, others 3.3V
  Routing 5V into a 3.3V device is usually bad
  Level translation may be required
Learn to interpret the component datasheets
  Look at min/max voltages and currents
  May provide sample circuits that illustrate use of a particular component
Invest in a multimeter for measuring voltages, currents, resistance, and continuity

## Slide 33: Cyber-Physical Systems: Circuit Hints
Most processor General Purpose Input/Output (GPIO) pins are not designed to drive low impedance/low resistance loads
  Relay, solenoid, and motor coils require a driver circuit that can supply more current than the GPIO pins
  LEDs typically require a series resistor to limit current draw
    Resistor too large allows too little current flow (dim LED)
    Resistor too small or non-existent allows too much current flow (bad)
  Failure to limit current sourcing/sinking through GPIO pins may result in permanent damage to the Raspberry Pi (or Arduino)
Relay/solenoid coils may require a parallel diode to dissipate back EMF (current flowing from collapsing magnetic field)

## Slide 34: Circuit Components – Resistors - 1
+ V -
I
+ V -
I
Ohm’s Law
Voltage = Current x Resistance
V = I x R
I = V / R = 3.3 volts/1000 ohm = 3.3 milliamps (mA)
I = V / R = 5.0 volts/1000 ohm = 5.0 milliamps (mA)
Current calculations for 1k ohm resistor with 5 V and 3.3 V circuits

## Slide 35: Circuit Components – Resistors - 2
https://learn.sparkfun.com/tutorials/resistors
Sample output from online resistance calculator at URL below
Photograph of 1 kOhm resistor
https://sites.google.com/site/kmitl58010166/home/lab-i-basic-resistive-circuit-calculations-and-measurements

## Slide 36: Circuit Components - Diodes
https://cdn.sparkfun.com/assets/learn_tutorials/7/5/backwardsDiode.png
Light Emitting Diode (LED)
Signal Diode
https://www.electronics-tutorials.ws/diode/diode_4.html
“one-way current check valve”

## Slide 37: Circuit Components - Pushbuttons
https://components101.com/switches/push-button
Switch Open
(Normally Open)
Switch Closed
(Switch Pressed)
A
B
A
B
A
B
A
B

## Slide 38: Hints for Instructors

## Slide 39: How are these circuits different?
OpenPLC Raspberry Pi
+V
PB1
PB2
R1
IN
OUT
R2
LED1
+V
OpenPLC Raspberry Pi
PB1
PB2
R1
IN
OUT
R2
LED1
+V
OpenPLC Raspberry Pi
PB1
PB2
R2
IN1
OUT
R3
LED1
IN2
R1

## Slide 40: Logical AND Defined by Circuit Geometry
OpenPLC Raspberry Pi
+V
PB1
PB2
R1
IN
OUT
R2
LED1
PB1 | PB2 | IN
Open | Open | 0
Open | Closed | 0
Closed | Open | 0
Closed | Closed | 1
IN = PB1 AND PB2

## Slide 41: Logical OR Defined by Circuit Geometry
+V
OpenPLC Raspberry Pi
PB1
PB2
R1
IN
OUT
R2
LED1
PB1 | PB2 | IN
Open | Open | 0
Open | Closed | 1
Closed | Open | 1
Closed | Closed | 1
IN = PB1 OR PB2

## Slide 42: Ladder Logic Defines PB1/PB2 Relationship
+V
OpenPLC Raspberry Pi
PB1
PB2
R2
IN1
OUT
R3
LED1
IN2
R1
PB1 | PB2 | IN1 | IN2
Open | Open | 0 | 0
Open | Closed | 0 | 1
Closed | Open | 1 | 0
Closed | Closed | 1 | 1
Build one circuit
Ladder Logic can create AND, OR, XOR, etc.

## Slide 43: Ladder Logic - Logical AND Operation
+V
Raspberry Pi
PB1
PB2
R2
IN1
OUT
R3
LED1
IN2
R1

## Slide 44: Ladder Logic - Logical OR Operation
+V
Raspberry Pi
PB1
PB2
R2
IN1
OUT
R3
LED1
IN2
R1

## Slide 45: Ladder Logic – XOR Function Block
+V
Raspberry Pi
PB1
PB2
R2
IN1
OUT
R3
LED1
IN2
R1

## Slide 46: Ladder Logic – Complex Functional Block
+V
Raspberry Pi
PB1
PB2
R2
IN1
OUT
R3
LED1
IN2
R1

## Slide 47: References
The OpenPLC Project
  https://www.openplcproject.com/
OpenPLC Editor
  https://github.com/thiagoralves/OpenPLC_Editor
Horowitz and Hill, The Art of Electronics 2nd ed.
  Good overview of digital and analog circuits with many examples including interfacing to sensors and actuators such as those in a cyber-physical system

## Slide 48: Hands-On Laboratory Exercise #5

## Slide 49: Laboratory Exercise #5 Instructions - 1
Objectives
  Practice using the OpenPLC toolchain (OpenPLC editor, OpenPLC runtime, and ScadaBR) to implement and test the alternative ladder logic programs

## Slide 50: Laboratory Exercise #5 Instructions - 2
Implement and test the alternative ladder logics presented in this lecture for the First Project physical circuit
  PB1 AND PB2
  PB1 OR PB2
  PB1 XOR PB2
  PB1 (with 2 sec dwell ON) OR PB2
https://www.openplcproject.com/reference-your-first-project

## Slide 51: Laboratory Exercise #4 Instructions - 3
Demonstrate HMI operation by replicating all possible push button states (as previously done with the simulator) but this time you will be using the physical circuit buttons for all ladder logics implemented
https://www.openplcproject.com/reference-your-first-project

## Slide 52: Laboratory Exercise #5 Instructions - 4
Sample Deliverables
  Zip file of entire project directory including structured text code
  Screenshots of Ladder Logic implemented and generated structured text
  Screenshots of HMI output for each possible combination of input states